EX-9132BI(Ver.5.0)

Introduction

*Support Bluetooth 5.0

*Maximum Packet size 250 bytes

*Transmission range up to 100 Meters

*Built in 15KV ESD protection for signals

*RS-422/485 surge protection

*Windows Configuration Utility

# Text boxes

Software Feateures

SET UP                       PC Site Utility / AT command

Power

Input                             DC 9 ~24V, 50mA@ 12VDC

Connector                    DC Jack & Terminal block

LED                             SYS Pairing, Rx, Tx

Specification

CPU	ARM Cortex M4 32 bit CPU, 64 MHz

Memory	1MB Flash ROM, 256K RAM

Bluetooth Module           Nordic NRF 52840

Bluetooth 5.0                 Operate in 2.4GHz~2.483GHz ISM Band

-95dBm sensitivity in 1Mbps Bluetooth low energy Mode

+8 dBm TX power(down to -20 dBm in 4dB

Steps)

Support Bluetooth Data Rate 1Mbp/s

Operating Distance up to 100 Meters

Security : 128-bit AES

Serial Ports                    RS-232 or RS-422/RS-485 * 1 Port (auto detect)

RS-232     Rx , Tx , GND , RTS , CTS

RS-422     Tx+ , Tx-, Rx+ , Rx-(Surge Protect)	S

RS-485     T Data+ , Data-(Surge Protect)

Built –in      RS-485 pull high / Terminal  Resistor

Speed       4800 bps~115.2 Kbps

Parity        None, Even

Stop Bit    1

Environment

Temperature               Operating   -10°C ~ 70°C (14°F ~ 158°F)

Storage: -25°C ~ 80°C (-13F ~ 176°F)

Humidity                      Operating   10% ~ 95% non-condensing

Storage: 5% ~ 95% non-condensing

Order Information:

Optional :                   Din-Rail mounting kits

Power supply(Linear/ Swintching)

Accessories :             CD(Utility/ Exbrowser ; IP Search; Virtual COM)

Relative products:     EX9133C-2/ PoE; EX9133C-2-MTCP;

EX9133C-RS232/ PoE; EX9133C-RS485/ PoE